CHLORIDE REDUCTION IN AEROBIC LEACHATE TREATMENT

Ketil Haarstad, Trond Mæhlum

Jordforsk, Centre for Soil and Environmental Research, F. A. Dahls v. 2, N-1432 Ås.

Chloride (Cl) is often regarded as inert and used as a tracer in transport calculations of groundwater plumes and estimation of dilution in ponds and wetland treatment systems. This experiment simulated aerobic treatment to study if observed field reduction rates of Cl can be duplicated in the laboratory, and also to investigate if some of the most probable chemical or physical factors significantly influence this reduction. The experiment used three real leachates and eight artificial leachate samples with varying concentrations of Cl, organic C, Tot-N and Fe in addition to three control samples. Leachate samples were collected from two landfills with municipal solid waste. Some of the samples were centrifuged after respiration to study the effect of particle separation. The oxygen consumption in the leachate samples was considerably lower than in the artificial samples, probably due to inhibitory compounds in the leachate. Mean Cl reduction was 22% for the leachate samples, 46% in the artificial samples and 10% in the controls. Only TOC concentration had significant influence on the oxygen consumption in the respirometer, both when measured in the artificial samples (p< 0.036) and for all samples (p<0.013). Oxygen consumption was the only significant factor (p< 0.0079) for Cl reduction. Centrifugation showed a significant effect on Cl reduction, both measured as reduction of electrical conductivity (p<0.002) and as Cl concentration (p<0.001). The reduction of Fe was low in the experiment, but was strongly influenced by centrifugation. Also the reduction of TOC and N was influenced by centrifugation. The reduction of Cl in aerobic treatment may be dependent on the formation of particles.

Key words—aerobic leachate treatment, respirometry, chloride reduction, dilution

# 1. Introduction

Chloride (Cl) is the most abundant halogen on earth, it constitutes 305 ppm. of igneous rocks and carbonates, and 170 ppm. of shales (Hem, 1985). Both Cl and Br atoms occur in various classes of minerals such as halides, oxides and hydroxides, but not in silicates (Flury and Papritz, 1993). In water more than three-fourths of the chloride element is in the oceans, where the average concentration is 19000 mg/l, in contrast to freshwater where typical concentrations are 1 to 1000 mg/l in groundwater (Todd, 1980), and 1 to 200 in surface waters (Stumm and Morgan, 1996). Cl represents about 0.07 to 0.21% of the in situ mass of municipal solid waste (MSW), with 0.18% being the expected leachable Cl (Rowe, 1993). Cl in leachate in Norway varies from <100 to 3000 mg/l (Haarstad et al., 1998). Measurements from UK shows variation between 500 to 5000 mg/l (Robinson, 1998).

The Cl anion is the only form of major significance of the element chlorine in water exposed to the atmosphere. Cl do not significantly enter into oxidation or reduction reactions, form no important solute complexes with other ions unless the Cl concentration is extremely high, do not form salts of low solubility, are not significantly adsorbed on mineral surfaces, and play few vital biochemical roles (Hem, 1985). Cl forms ion pairs or complex ions with some of the cations present in natural waters, but these are not strong enough to be of significance in the chemistry of freshwaters, but can be in seawater and brines (Hem, 1985). Cl can be removed from the water phase in three ways: oxidation to free chlorine, by precipitation and by complexation, basically with organometallic compounds.

Cl is considered as a conservative (non-reactive) anion and is often used as a tracer in water transport experiments and studies. Measurements of Cl concentrations has been used to estimate hydrological pathways (Peters and Ratcliffe, 1998, Sukhija et al., 1996), evapotranspiration (Claasen and Halm, 1996), transport of herbicides in soils (Thomas and Swoboda, 1970, McMahon and Thomas, 1974, Flury et al., 1995, Seaman et al., 1995, Ishiguro et al., 1992, Lockwood et al., 1995), contamination from septic systems (Robertson et al., 1991), and to measure residence time in trickling filters (Gray, 1981, Robertson et al., 1991). Claasen and Halm (1996) reported that the Cl method agreed within 10% of control methods to calculate evaporation in 13 of 19 watershed studies.

Extensive leachate treatment systems based on holding dams, aeration ponds, phytotreatment and filtration experience show Cl reduction in the range of 30-55%, of which the aerobic step constitutes more than 90% (Mæhlum, 1998).

Figure 1. Time series of Cl concentrations in two leachate treatment systems (right: Esval landfill, left: Bolstad landfill).

Typical sizes of the aeration pond of leachate treatment systems in Norway is 2000 to 4000 m3, with a corresponding mean hydraulic retention time of 20 to 40 days, and a mean hydraulic loading rate (HLR) of 40 to 80 mm d-1 (Mæhlum and Haarstad, 1997). If the reduction of Cl in treatment systems is caused by dilution, this has to be corrected for when calculating the reduction of pollutants. The hydrological budget, including precipitation, evapotranspiration, surface runoff and groundwater transport, can not explain the high reduction rates of Cl in most cases. If, on the other hand, Cl is removed from the aqueous phase, correction due to dilution is not necessary. The objective of this experiment was to simulate aerobic treatment to investigate if the field reduction rates can be duplicated in the laboratory, and to study if some of the most probable chemical factors; Cl, TOC, Fe and Tot-N, and physical factors; electrical conductivity, oxygen consumption and pH, significantly influence this reduction.

# Materials and methods

The experiment is based on measurements of electrical conductivity before and after aeration of 200 ml. samples in a BI-1000 Electrolytic Respirometer from Bioscience, Inc. The electrical conductivity was measured with a Phillips Digital Conductivity meter PW 9527. pH was measured with an Orion Ross pH-electrode no. 91555C, and a Hanna Instrument HI 931402, no. 008604. Reducing conditions have been established in all samples prior to aeration with 1 mg/l ditionid and with 0.3 mg/l resazurin as an indicator of anaerobic conditions (Nannipiesi and Alef, 1995). This was not done for the controls. Analytical chloride was measured with a Dionex QIC Ionic Chromatograph Analyzer with detection limit 0.5 mg/l, total nitrogen (Tot N) with a Technicon Traacs 2000, iron (Fe) on a Perkin Elmer 3000DV, and total organic carbon (TOC) on a Dohrmann DC-190 high temperature TOC analyzer. All analytical methods are accredited according to NS150. Norton et al. (1996) reported that colorimetric Cl data depends on carbon concentrations, but not ion chromatographic data, and only for concentrations up to 100 eq/l dissolved organic carbon.

Three types of raw leachate samples were collected from two MSW landfills; the Dal Skog landfill and Esval landfill. Leachate characteristics are given in Table 1

Table 1. Mean leachate characteristics (Haarstad et al., 1998), and samples used in the experiment. Units in mg/l except pH, and conductivity = S/cm.

|  | Dal Skoga Young | Dal Skog Young, exp. | Dal Skog Old | Dal skog Old, exp. | Esval | Esval exp. |
| --- | --- | --- | --- | --- | --- | --- |
| pH | n.m. b | n.m. | 6.3 | n.m. | 7.1 | n.m. |
| El. Cond. | 15480 | 6414 | 7460 | 6770 | 6800 | 4817 |
| Cl | 2236 | 1880 | 1290 | 2090 | 1000 | 892 |
| COD | n.m. | 871c | 7105 | n.m. | 2766 | 1240c |
| TOC | 9090 | 1100 | 2484 | 1120 | 1125 | 304 |
| Tot-N | n.m. | 340 | 213 | 356 | 239 | 247 |
| NH4-N | 645 | n.m. | 200 | n.m. | 173 | n.m. |
| Fe | 1647 | 138 | 510 | 154 | 59 | 31 |

aYoung=recent part of landfill, old=old part of landfill, exp.= samples from this experiments, bn.m.=not measured, c measured as oxygen consumption during respirometer experiment

The experiment consisted of 3 leachate types in duplicates, 8 artificial samples and 3 controls with varying concentrations of Cl, see Table 2.

Table 2. Experimental layout a. Concentrations (mg/l) before aeration

a Samples labelled 1 are from the Dal Skog landfill, sample 2 is from Esval landfill, samples labelled 3 are artificial leachate samples: the four 1-digits with + or – signs indicate high and low concentrations of Fe, TOC, Tot-N and Cl, respectively, samples labelled 4 are controls with different Cl concentrations

Artificial leachate samples were produced in order to study the impact by varying four factors: Fe, TOC, Tot-N and Cl with concentrations according to Table 2, where a “–1” denotes low level, and “1” denotes high levels for the factors. These factors are usually responsible for the majority of the variation in a typical MSW leachate. The sample orders were designed as a 2-level design with 4 factors. Multiple differences between means was analysed by the Tukey-Kramer HSD-test, differences between paired observation, e.g. samples before and after centrifugation, were tested by either by the student-t test or the Wilcoxon Signed-Rank test (JMP, 1995).

In the artificial leachate samples TOC was prepared with D-glucose (C6H12O6), Cl with KCl, nitrogen with (NH4) 2HPO4, and Fe with FeSO4*7H2O. All samples were shaken for 2 hours in room temperature. Selected samples were centrifuged for 15 minutes after respiration at 7500 rpm, to see if the reduction of Cl and electrical conductivity was dependent on particle attraction. The reduction of compounds in the samples was calculated as:

R = 1 – (Cout/Cin)			(1)

where Cout is concentration after experiments, and Cin is concentration before experiments.

# Results

The relation between electrical conductivity and measured Cl concentrations indicate that electrical conductivity increases 9% faster with Cl concentration in leachate samples than in water samples (Figure 2).

The correlation between measured electrical conductivity and Cl was tested in 15 samples. The correlation is statistically significant both for the total Cl range used in the experiments.

Figure 2. Correlation between electrical conductivity and Cl concentrations in natural waters (Hem, 1985), and in the tested leachate samples

The respirometer measures the oxygen consumption in the sample during aeration, and the final accumulated results are shown in Table 2. One of the samples with leachate from Esval failed due to pollution of the sample from KOH in the CO2-trap of the respirometer. Measurements of oxygen consumption in the other sample from Esval together with sample 2’6 failed due to malfunction of the readout unit of the oxygen electrode. There is, however, no reason to believe that the aeration of these samples failed. The control samples showed an accumulated oxygen consumption of 252 to 370 mg/l, which can be considered as a noise level in measurements of oxygen consumption. The oxygen consumption in the leachate samples was considerably lower than in the artificial samples, probably due to inhibitory compounds in the leachate. This has also been shown earlier, especially in the Esval samples (Haarstad and Mæhlum, 1998). There was a tendency to faster oxygen in the samples with low TOC, but the final oxygen consumption is higher in samples with high TOC (Figure 3).

Table 3. Oxygen consumption in experiments a

aLabels explained in Table 2.

Figure 3. Oxygen consumption in artificial samples (thin lines = low TOC, heavy lines = high TOC). Sample labels are explained in Table 2.

The reduction of electrical conductivity and Cl concentrations is shown in Table 4. There was no significant difference between the reductions, but there was a significant difference between leachate samples and controls, see Figure 4.

Table 4. Electrical conductivity (S/cm) and Cl in samples before and after aeration in the respirometer, and estimated reduction R (see Eq. 1). a

a Labels explained in Table 2.

Figure 4. Significant difference in removal of Cl between artificial (art), control (ctrl)  and experimental (exp) samples. Non-intersecting circles indicate significant difference at p<0.05, horizontal line show the overall mean

Mean Cl reduction, based on measurements of electrical conductivity and Cl concentrations, respectively, was 17% and 22% for the leachate samples, 22% and 28% for the artificial samples and -2% and –5% in the controls. Non-overlapping circles in Figure 4 illustrate significant differences.

Only TOC showed significant influence on the oxygen consumption in the respirometer, both when measured in the artificial samples (p< 0.036) and for all samples (p<0.013). There were too few leachate samples to analyse the dependency on oxygen consumption.

Cl can be removed from the water phase in three ways: oxidation to free chlorine, by precipitation and by complexation, basically with organometallic compounds. Only the latter can be considered realistic for the concentration range and physiochemical environment considered here. Iron is available for complexation if the solution is acidic. pH in the samples varied from 6.3 to 7.9, see Table 2. pH showed a significant influence on Cl reduction (p<0.038), when tested simultaneously with Cl, Fe, TOC, Tot-N. The reduction increases with pH (Figure 5), indicating that iron-organic complexes are not the explaining factor. This was, however, not confirmed by the TOC and Fe measurements.

Figure 5. Cl reduction dependence of pH.

Oxygen consumption was the only significant factor (p< 0.008) influencing the reduction of Cl, both when measured as Cl concentrations or indirectly as electrical conductivity.

The mean HLR in leachate aerobic treatment systems is usually low, 40 to 80 mm d-1 (Mæhlum and Haarstad, 1997). If the reduction of Cl experienced in such systems were dependent on particle attraction the Cl reduction should be influenced by centrifugation. The reduction of electrical conductivity in 12 centrifuged samples was 12% higher than in non-centrifuged samples (p<0.004). The reduction of Cl in 7 centrifuged samples was 74% higher than in non-centrifuged samples (p<0.001) with a non-parametric Signed-rank test). The reduction of Fe was highly dependent on centrifugation, with insignificant values for non-centrifuged values, and a reduction of 0.89 for artificial samples and 0.95 for leachate samples. Also TOC and N seemed influenced by centrifugation, with a TOC reduction of 0.69 before, and 0.81 after centrifugation and N reduction of 0.20 before and 0.34 after centrifugation, but the differences were not significant. With a significant effect of centrifugation on Cl reduction, sedimentation processes can effect Cl concentration in large aeration ponds.

# Conclusions

- Mean Cl reduction was 22% for the leachate samples, 46% in the artificial samples and 10% in the controls.

- Only TOC showed significant influence on the oxygen consumption in the respirometer, both when measured in the artificial samples (p< 0.04) and for all samples (p<0.01).

- Oxygen consumption was the only significant factor (p< 0.01) for Cl or electrical conductivity reduction.

- The reduction of Cl concentration was 74% higher in centrifuged samples, and electrical conductivity was 12% higher after centrifugation compared to non-centrifuged samples. The reduction of Fe was low in the experiment, but was high after centrifugation.

- Cl reduction was higher at high pH

- The oxygen consumption in the leachate samples was considerably lower than in the artificial samples, probably due to inhibitory compounds in the leachate. There was a tendency to faster oxygen in the samples with low TOC, but the final oxygen consumption is higher in samples with high TOC.

- It is not possible to conclude that complexing reactions with organic matter are responsible for Cl reduction in the experiments, although these are the most probable processes

# Research needs

Based on the findings in our studies we believe that a more comprehensive knwoledge of the chemical processes behind chloride reduction in leachate treatment system is needed, and probably aimed at organic - metal complexing reactions.

# Acknowledgements

We would like to thank the Department of Agriculture and the Department of Environment for granting strategic research funding for this project. Thanks are due also to the administration at the Esval and Dal Skog landfills for the supply of leachate samples and historical data on leachate characteristics, and to E. Steinnes at the Norwegian University of science and technology for valuable comments.

# References

Claasen, H. and Halm, D.R. (1996) Estimates of evapotranspiration or effective moisture in Rocky Mountain watersheds from chloride ion concentrations in stream baseflow. Water Resour. Res., 32, 2, 363-372.

Flury, M. and Papritz, A. (1993) Bromide in the Natural Environment: Occurrence and Toxicity. J. Environ. Qual. 22: 747-758.

Flury, M., Leuenberger, J., Studer, B. and Fluhler, H. (1995) Transport of anions and herbicides in a loamy and a sandy field soil. Water Resour. Res., 31, 4, 823-835.

Haarstad, K. and Mæhlum, T. (1999) MSW leachate variability and alternative pre-treatment filter in cold, temperate climates. In (Christensen, T., Cossu, R. and Stegmann  R., Eds.): Leachate, Gas, operation and health effects in landfills. Proceedings Sardinia 99, Vol. II, pp. 215-224, CISA, Via Marengo 34, I-09123 Cagliari.

Haarstad, K. and Mæhlum  T., Kraft, P. (1998) Dannelse, utslipp og prøvetaking av sigevann fra kommunalt avfall. Vann, 1, 60-80 (in Norwegian).

Hem, J.D. (1985) Study and Interpretation of the Chemical Characteristics of Natural Water. Third Edition, US Geological Survey Water-Supply Paper 2254, 263 pp., Distribution Branch, Text Production Section, USGS, 604 South Pickett St., Alexandria, VA 22305.

Ishiguro, M., Song, K-C. and Yuita, K. (1992) Ion Transport in an Allophanic Andisol under the Influence of Variable Charge. Soil Sci. Soc. Am. J., 56, 1789-1793.

JMP. (1995) JMP Statistics and Graphics Guide, Version 3. 593 pp. SAS Intitute Inc., Cary, NC, USA.

Lockwood, P.V., McGrity, J.W and Charley, J.L. (1995) Measurement of chemical weathering rates using natural chloride as tracer. Geoderma, 64, 215-232.

McMahon, M.A. and Thomas, G.W. (1974) Chloride and Tritiated Water Flow in Disturbed and Undisturbed Soil Cores. Soil Sci. Soc. Amer. Proc., 38, 727-732.

Mæhlum, T. and Haarstad, K. (1997) Leachate treatment in cold climate. In (Christensen, T., Cossu, R. and Stegmann, R., Eds.): Leachate and landfill gas management. Proceedings Sardinia 97, Vol. II, pp. 337-344, CISA, Via Marengo 34, I-09123 Cagliari.

Mæhlum, T. (1998) Cold-climate constructed wetlands: Aerobic pre-treatment and horizontal subsurface flow systems for domestic sewage and landfill leachate purification. Dr. Scient. Thesis 1998:9, NHL, 1430 Ås, 163 pp.

Nannipiesi, P. and Alef, K. (Editors). (1995) Methods in applied soil microbiology and biochemistry. London, Academic Press, 576 pp.

Norton, S.A., Handley, M.J., Kahl, J.S. and Peters, N.E. (1996) Re-evaluation of colirometric Cl data from natural waters with DOC. Water, Air and  Soil Pollution, 91, 283-298.

Peters, N. and Ratcliffe, E.B. (1998) Tracing hydrological pathways using chloride at the Panola Mountain research watershed, Georgia, USA. Water, Air and Soil Pollution, 105, 263-275.

Robertson, W.D., Cherry, J.A. and Sudicky, E.A. (1991) Ground-Water Contamination from Two Small Septic Systems on Sand Aquifers. Ground-Water, 29, 1, 82-92.

Robinson, H. (1998) Leachate composition from different landfills. Proceedings of the International Training Seminar: Management and Treatment of MSW Landfill Leachate, Venice, 2-4 December 1998, CISA, Via Marengo 34, I-09123 Cagliari, pp. III 1-13.

Seaman, J.C., Bertsch, P.M. and Miller, W.P. (1995) Ionic tracer movement through highly weathered sediments. J. of Contaminant Hydrology, 20, 127-143.

Stumm, W. and Morgan, J.J. (1996) Aquatic Chemistry. 3rd Edition, John Wiley & Sons, Inc., New York, NY, pp. 873.

Sukhija, B.S., Reddy, D.V., Nagabhushanam, P., Hussain, S., Giri, V.Y. and Patil, D.J. (1996) Environmental and injected tracers methology to estimate direct precipitation recharge to a confined aquifer. Journal of Hydrology, 177, 77-97.

Thomas, G.W.and Swoboda, A.R. (1970) Anion exclusion effects on chloride movements in soils. Soil Science, 110, 3, 163-166.